## Slide 1: Tips for Phase & Time Sync A case study with Orange Egypt
Ahmed Medhat, Oscilloquartz
Sherif Fouad, Orange Egypt

## Slide 2: Outline
Case study of a collaborative project between Orange Egypt and Oscilloquartz
Project objective: evolution of synchronization from TDM-frequency to PTP-phase
Evolution in phases
Constraints from the existing transport network and its evolution potential
Testing: can the performance objectives be met?
Comparison of PTP profiles for phase
Conclusions and future work

## Slide 3: Initial situation: TDM sync network / frequency
2G/3G TDM Site
Core Site
SSU
Cesium
BITS Clk
GNSS
Cesium Based PRC System
Core Elements
BITS Clk
Remote BSC/RNC Sites
GNSS Receiver
BITS Clk
GNSS
GNSS Based PRC System
BSC/RNC
BITS Clk
SDH Backbone Cloud
3rd Party
MW Access Cloud
Orange Property
2G/3G TDM Site
MW Access Cloud
Orange Property
BSC/RNC
MGW
MSC
3rd party STM Clk

## Slide 4: 1st evolution: SyncE sync network / frequency
2G/3G IP Site
Core Site
SSU
Cesium
BITS Clk
GNSS
Cesium Based PRC System
Core Elements
SyncE
Remote BSC/RNC Sites
GNSS Receiver
SyncE
GNSS
GNSS Based PRC System
BSC/RNC
BITS Clk
MW Access Cloud
Orange Property
2G/3G IP Site
MW Access Cloud
Orange Property
BSC/RNC
MGW
MSC
3rd party STM Clk
SyncE
SyncE
IP Backbone Cloud
3rd Party
SyncE
SyncE ports
SyncE ports

## Slide 5: 2nd evolution: PTP sync network / frequency
MW Access Cloud
Orange Property
2G/3G/4G IP Site
Core Site
SSU
Cesium
BITS Clk
GNSS
Cesium Based PRC System
Core Elements
G.8265.1
Remote BSC/RNC Sites
GNSS Receiver
G.8265.1
GNSS
GNSS Based PRC System
BSC/RNC
BITS Clk
MW Access Cloud
Orange Property
2G/3G/4G IP Site
BSC/RNC
MGW
MSC
G.8265.1 back up from Core GM
G.8265.1
G.8265.1
IP Backbone Cloud
3rd Party
G.8265.1
HDSL Cloud
3rd Property
2G/3G/4G Small Cell IP Site
G.8265.1
G.8265.1
G.8265.1
G.8265.1

## Slide 6: Test 1: Macro Node-B via MW link with G.8265.1
PASSED
6 MW

## Slide 7: Test 2: Small Cell via HDSL link with G.8265.1
PASSED

## Slide 8: 3rd evolution: heading towards PTP phase sync
Intention to prepare the network infrastructure for phase synchronization in view of new LTE-A features such as Carrier Aggregation, COMP, eICIC
The following PTP options were considered:
  ITU-T G8275.1 (Full On Path Support)
  ITU-T G8275.2 (Partial On Path Support)
Limitations in Orange’s access network:
  MW vendor A: MW systems “A1” cannot be upgraded, systems “A2” can be upgraded (software, license)
  MW vendor B: existing “old” MW system cannot be upgraded to support BC; BC only with replacement by “new” MW systems
Partial on path support Profile ITU-T G8275.2 was our closest solution to be tested with above limitations

## Slide 9: Test sequence 1: MW vendor “A” & G.8275.2
6OCT-WDY-NKL
SADAT BSC
PTP APTS
BITS Clk
GNSS
GNSS Based PRTC System
BSC/RNC
MW Access Cloud
6 MW Hops
G.8265.1 & G.8275.2
G.8265.1 & G.8275.2
G.8265.1
G.8265.1 back up from closest Core GM
Router
Slave/Probe
G.8275.2
Get closer when TE> 1.1 us
G.8275.2 (MW Only)
Bypass IP router to enhance margin

## Slide 10: Results test sequence 1 (vendor “A”)
FAILED
FAILED
TE collected over 6 MW links + 1 Router
TE collected over 2 MW links + 1 Router

## Slide 11: Results test sequence 1 (vendor “A”) Cont.
FAILED
TE collected over 3 MW (Bypassing Router)
TE collected over 2 MW links (Bypassing Router)
PASSED

## Slide 12: Test sequence 2: MW vendor “B” & G.8275.2
NBRYA-WST-1
Amerya BSC
PTP APTS
BITS Clk
GNSS
GNSS Based PRTC System
BSC/RNC
MW Access Cloud
7 MW Hops
G.8265.1 & G.8275.2
G.8265.1 & G.8275.2
G.8265.1
G.8265.1 Back up from closest Core GM
Router
Slave/Probe
G.8275.2
Get closer when TE> 1.1 us
G.8275.2
Bypass IP router to enhance margin

## Slide 13: Results test sequence 2 (vendor “B”)
TE collected over 5 MW links (Bypassing Router)
TE collected over 2 MW links (Bypassing Router)
FAILED
FAILED

## Slide 14: Results test sequence 2 (vendor “B”) Cont.
TE collected over 1 MW link (Bypassing Router)
PASSED

## Slide 15: Phase POC summary and way forward
G8275.2 PTP profile can be used over maximum 1 (vendor B) or 2 (vendor A) MW hops
Enabling G8275.1 BC is the only way to deliver phase over longer MW chains
MW vendor A:
  Upgrade all “A2” MW systems for BC support
  Replace all “A1” MW systems (not upgradeable) with new A2 systems with BC Support
MW vendor B
  Replace the “old” MW systems (not upgradeable) with the “new” systems with BC Support
  OSA to Propose “Intermediate” cost effective Solution to enable phase delivery on hybrid chains until completing the full MW swap to “new” MW system
Schedule further tests to prove G.8275.1 performance

## Slide 16: 3rd evolution option 1: SFP Sync Plug@ “old” MW Vendor “
This scenario is not recommended as the PTP will encounter asymmetry on the old MW links
PTP G8275.1
PTP G8275.2
“New”
“New”
“”old””
“”old””

## Slide 17: 3rd evolution option 2: SFP Sync Plug @ “new” MW links
This scenario recommended as the PTP will not encounter asymmetry
PTP G8275.1
PTP G8275.2
PTP G8275.1

## Slide 18: Conclusions
Extensive performance testing was necessary to verify PTP Frequency/Phase whether existing network infrastructure is able to transport synchronization with the required performance
G.8275.2 PTP profile proved inadequate in microwave access network
G.8275.1 in the access network is the way to go in this case
Further tests with G.8275.1 are under way