## Slide 1: Synchronisation Challenges in Next Generation RRUs
©2018 Rakon Limited
Advanced Timing for
High Speed Connectivity

## Slide 2: Contents
Traditional Base Station Sync
Evolution of 5G and Front-Haul technologies
Sync Architectures for next generation RRUs
Air Interface clocking for 5G RRUs

## Slide 3: 4G Base Station Clocking functions
BBU
RRU
RRU
T-GM - Telecom Grand Master, BBU – Base Station Unit, RRU – Remote Radio Unit
T-GM
T-GM
Backhaul
Front-haul
CPRI
RRU
Base Station Clock Supports
Clock recovery
  GNSS
  Physical Layer
  Packet Layer
Holdover
Radio Clock Supports
Clock recovery
  CPRI layer
Air Interface requirements

## Slide 4: Traditional Clocking Implementations
RRU
CPRI
RF PLL
VCXO
DAC & PA
ADC & LNA
Filters
BBU
Timing & Sync
External Clocks
OCXO
Processor Subsystem
Base Band
Network Interface Processing
GNSS
1PPS
Packet I/O
SyncE
CPRI

## Slide 5: Next Generation - Physically disconnected RRUs
eCPRI supports Ethernet-switched IP-routed front-haul networks, or similar types of transport networks
CU
CU
CU
CU
AU
eCPRI
DU
DU
RRU
RRU
T-GM - Telecom Grand Master, CU – (Centralized) Cloud Unit, DU – Distribution Unit, AU – Access Unit
T-GM
T-GM
Backhaul
Fronthaul I
Fronthaul II
Ethernet
GNSS

## Slide 6: 5G Cellular Synchronisation requirements
3GPP requirements
  Air Interface
  Network Interface
    16ppb
Holdover
  Hold previously known
  For x hours/days
Advanced features
  COMP, ICIC
LTE (FDD and TDD) | Wide Area | 50ppb |  | 3GPP TS 36.104 [7] Clause 6.5.1 | Frequency accuracy at the air interface, over one sub-frame period (1ms)
 | Med. Range | 100ppb |  |  | 
 | Local Area | 100ppb |  |  | 
 | Home | 250ppb |  |  | 
LTE-TDD | Wide area, >3km radius |  | 10µs | 3GPP TS 36.133 [8] Clause 7.4.2 | Maximum deviation in frame start times at the air interface (for cells on the same frequency with overlapping coverage areas)
 | Wide area, ≤3km radius |  | 3µs |  | 
 | Home BS, >500m rad. |  | 1.33 + Tprop µs |  | 
 | Home BS, ≤500m rad. |  | 3µs |  | 
[1] Tprop is the propagation delay between the Home BS and the cell selected
as the network listening synchronisation source
5G will use the 4G synchronisation requirements for now

## Slide 7: Transport Network requirements - Sync
Transport Network Synchronisation
  Packet Sync Mechanisms such as IEEE1588
  With or without SyncE
2 Cases for Deployment Scenarios
  Case 1 : Packet clock integrated into eRE
  Case 2 : Packet clock at the network edge
    1PPS/ToD to eREs
Category | ¦TE¦ for case 1& 2 | Applications Details | TAE proposed by IEEE801.CM |  | TAE (for Application)
 |  |  | Case 1 | Case 2 | 
A+ | TBD | MIMO or TX diversity transmissions, at each carrier frequency | - | 20ns | 65ns
A | TBD | Intra-band contiguous carrier aggregation, with or without MIMO or TX diversity | 60ns | 70ns | 130ns
B | TBD | A & Inter-band carrier aggregation, with or without MIMO or TX diversity | 100ns | 200ns | 260ns
C | 1100ns | 3GPP LTE TDD | 1100ns | 1100ns | 1500ns

## Slide 8: Challenges
Packet based timing recovery
Environmental Aspects
  Higher temperatures of operation
  Higher shock and reliability requirements
Higher Air interface spectral frequencies

## Slide 9: Environmental Effects
Higher Temperatures of operation
  Densification demands modular equipment configurations
Weatherproof outdoor equipment
  Fan-less, sealed enclosures designs
Massive MIMO RRUs
  Higher Power consuming radios
  PCBs getting hotter > 85degC
Outdoor deployments
  Lamp posts & structures
  Requires low shock & vibration
Reference Clocking challenges
  Higher temperature of operations
    All ASICs - special process solutions
    Specific components
Reference Clocking challenges
  Special designs resilient to shock & Vibration
    SC-cut strip crystal with G-sensitivity < 1ppb/G
    Enhanced performance in vibration prone environments

## Slide 10: 5G RRU timing evolution
Packet interface into RRU necessitates protocol layer timing recovery
Packet timing recovery needs higher stability reference clocks
CPRI
RF PLL
VCXO
DAC & PA
ADC & LNA
Filters
eCPRI/Ethe-rnet
RF PLL
VCXO
DAC & PA
ADC & LNA
Filters
PTP PLL
TCXO
OCXO

## Slide 11: Options for Synchronisation
Clocking scenarios
  GNSS based timing
  PTP with SyncE
  PTP with enhanced SyncE
  PTP with no SyncE
Worst Case PDV into the Radio
GNSS based timing
  1PPS synchronisation input
  Rule of thumb
    Loop filter < 1/10 of input clocking
  Typical loop bandwidths ~30mHz

## Slide 12: PTP with SyncE or Enhanced SyncE
Network Limit of G.8262/G.8262.1 from G.8261
*G.8262.1 may have a reduced network limit
Requirements

## Slide 13: Generalized approach for SyncE / eSyncE
Frequency offset = A * 2 * pi * fbw
To get a 20ppb ffo at the synchronizer output
The filter value needs to be 12mHz

## Slide 14: Worst Case Error across temperature
With 0.5ppb/degC
With 0.2ppb/degC
Assumptions :
- Wander generation with ideal input case, filter value 12mHz
- The radio may see a full range of temperature variations – 0.5degC/min
200+ns
80+ns

## Slide 15: RRU Synchronisation solutions
 | Frequency (Package size) | Stability (Temperature range) | Slope (ΔF/ΔT) | Aging (10 years) | Phase Noise (Typ. @ 19.2MHz)
TCXO | 10 – 40 MHz (5.0 x 3.2 mm) (7.0 x 5.0 mm) | ±50 ppb (-40 to 85°C) ±100 ppb (-40 to 105°C) | ±20 to ±10 ppb/°C | 3ppm | -123 dBc/Hz @100Hz -155 dBc/Hz @10kHz -156 dBc/Hz @ 100kHz
Key Features:
  Temperature stability : +/-50ppb (-40 to 85C)
  High temperature ranges : -55 to 105°C available
  <5ppb/degC temperature slope
  7mmX5mm
50ppb TCXO
Mini OCXO
Key Features:
  +/-10ppb (-40 to 85C) temperature stability
  9mmx7mm, 7mmx5mm next generation
  <0.5ppb/degC temperature slope
  High temperature ranges : 105°C available
  Fast Start-up times
 | Frequency (Package size) | Stability (Temperature range) | Slope (ΔF/ΔT) | Aging (10 years) | Phase Noise (Typ. @ 50 MHz)
Mini OCXO | 10 – 50 MHz (9.7 x 7.5 mm) (7.0 x 5.0 mm) | ±10 ppb (-40 to 85°C) ±20 ppb (-40 to 95°C) | ±1 to ±1.5 ppb/°C | 3ppm | -148 dBc/Hz @100Hz -154 dBc/Hz @10kHz -156 dBc/Hz @ 100kHz
Chart: Temperature (⁰C)
Chart: Frequency vs Temperature Orbit

## Slide 16: Radio Clock reference challenges
4G clocks cover up to 2.4GHz frequencies
5G covers high spectral frequencies
  Up to 100GHz
4G / LTE bands

## Slide 17: Contribution to EVM - Phase noise
Reference clock phase noise contributes to EVM
  As the modulation level increase (like 256 QAM) the constellations are dense, minimal close-in noise desired
Ideal Constellations
Constellations with high phase noise

## Slide 18: RF References for 5G
Higher spectral frequencies need low phase noise reference clocks – GHz VCXOs
eCPRI/Ethe-rnet
RF PLL
VCXO
DAC & PA
ADC & LNA
Filters
PTP PLL
TCXO
OCXO
RF PLL
GHz VCXO
CPRI
RF PLL
VCXO
DAC & PA
ADC & LNA
Filters

## Slide 19: High frequency clock references
Two clocking reference options
  Ultra low phase noise, low frequency
  Low phase noise, GHz frequency
Ultra low phase noise solutions
  122.88M VCXO
GHz frequency solutions
  ~2.5GHz VCXO solutions

## Slide 20: Conclusion
Next Generation Base station architectures poses synchronisation challenges for RRU implementations
Network clock recovery will be based on packet clock recovery methods, needs more stable reference clock than current
Environmental effects are critical
Higher spectral frequencies requires very low noise reference clocks for superior performance

## Slide 21: Acknowledgements
Dr. Nigel Hardy, Principal Design Engineer, Rakon UK Limited
Cyril Datin, R&D - Product Development Manager, Rakon France SAS
Florentin Margarit; Product R&D Engineering, Rakon UK Limited, New Zealand
References
IEEE P802.1CM/D2.2 Draft Standard for Local and metropolitan area networks—Time-Sensitive Networking for Front-haul
eCPRI Interface Specification: eCPRI Specification V1.1 - Common Public Radio Interface
CPRI Interface Specification : CPRI Specification V7.0 Common Public Radio Interface
eCPRI Transport Network D0.1 - Common Public Radio Interface: Requirements for the eCPRI Transport Network
IEEE1914.3/D3.2 : Draft Standard for Radio over Ethernet Encapsulations and Mappings

## Slide 22
Thank you
www.rakon.com