## Slide 1: Keeping Time with GNSS
?
Making the most of a best-effort service
Kenneth Hann, Senior Director R&D , Oscilloquartz
ITSF Nov 2018

## Slide 2: Motivation & Background (assuming need for for high accuracy time )
GNSS – wow!
  Ubiquitous, still developing, fragile
  5G, small-cell ... Power; Financial;...
High accuracy; low in network
  Integrated-GM Measurements
  Applicable to PRTC-B and ePRTC solutions
Securing time via GNSS
  Real abuse of GNSS
  Backup and monitoring are essential

## Slide 3: 1) GNSS – usually the only practical option for high accuracy time

## Slide 4: GNSS everywhere... With the same challenges
Regional Network
GNSS is a critical component of (almost) all time systems
PRTC
Local Network
PRTC
PRTC
Remote Dependence
Local Dependence
Embedded
Dependence

## Slide 5: GNSS is an enabler for fast rollout
GNSS is fast to deploy
No network upgrade
Meets tightest time synchronization requirements (<100ns)
Options:
  1) 2)
PRTC
Local Network
GNSS Equipment Integrated
GNSS + GM

## Slide 6: “Integrated GrandMaster”
Fast Deployment
Easy Installation - partial sky view
Standard Ethernet/Copper or Fibre (SFP)
(No RF-cabling required)
Outdoor (Pole/wall)
Indoor (window)

## Slide 7: RF delays – site specific compensation
OVP + (Line Amp)
PRTC
Antenna Vendor | Typical delay | Delay variation
A (commercial) | 23nsec | +/-15
B (commercial) | 19nsec | +/-10
C (high end) | 10nsec | +/-5
33ns
12ns
918ns
15ns
Accurate compensation of RF delays is difficult!

## Slide 8: Evolution to Integrated GrandMaster
Outdoors
Indoors
UTC
IOT GM
OVP + (Line Amp)
PRTC*
PTP
* PRTC includes GM function
Notes: Apart from removing the RF cable...
What’s different about an IOT PRTC?

## Slide 9: 2) High accuracy; low in network Measurements at National Lab.

## Slide 10: Testing at VTT MIKES
VTT provides UTC MIKES
Distance 876m
Fibre connection
PTP White Rabbit
Accuracy UTC ~5ns
Link to Finnish Time keeper VTT MIKES

## Slide 11: Antenna/GM testing locations at VTT #1 Indoor (glass bricks); #2 Outdoor (wall)
#1 Indoor
#2 Outdoor

## Slide 12: VTT Test results (~1 week) 5405 Outdoor
Time Error (ns) to UTC Mikes
TIE 35nsec
Modified Julian Day

## Slide 13: VTT Test results (~1 week) 5405 Indoor
Time Error (ns) to UTC Mikes
TIE 40ns
Modified Julian Day

## Slide 14: VTT Test results – MTIE / TDEV

## Slide 15: 3) Securing time from GNSS

## Slide 16: Improvements to GNSS technology
Civilian GNSS service remains best effort
Cost
Military / Government
Challenges
PRTC test from STRIKE3
Encrypted L2 GNSS receivers
CRPA antennas
Multiple GNSS constellations
GNSS L1 receiver certification (STRIKE-3)
Multiple Band GNSS receivers (e.g. L1 + L2 /L5)
Google – Raw data + analysis tools
GNSS Analysis Tools
from Google

## Slide 17: Essentials for robust time provisioning
Network protection/backup (no sole dependency on GNSS)
  Exact model depends on network (ownership; capabilities; asymmetry...)
ePRTC
Network
IOT GM
...
Grand
Master
GNSS
Core/Mobile Backhaul Provider
Mobile
Network Operator
High PDV/ Asymmetry
PTP Slave Clock
Slave
4G Base Station / Small Cell
Packet-Based
Backhaul Network
Grand
Master
GNSS

## Slide 18: GNSS Solution for high time accuracy
Local GM removes assymetries
  Cable and network
Simple installation
  Indoor or Outdoor
  “UTC out-of-the-box”
  Backup via network
Continous monitoring
  Network clock(s) V GNSS
  Other sync and GNSS KPIs
Network
IOT GM
ePRTC
(GNSS + Cs holdover)
Cs Stability
GNSS Accuracy
Note without the IOT GM the network asymmetry will usually exceed 1us

## Slide 19: Essentials for robust time provisioning
Monitor and correlate Key Performance Indicators (KPIs)
IOT-GM Monitoring | KPIs
GNSS data (raw?) | #Carrier locked Satelites SNRs; AGC Jamming, Spoofing, warnings
GNSS V PTP | MTIE (after assymetry correction)
GNSS V SyncE | MTIE
GNSS V OCXO | Freq offset (ppb)
ePRTC
Network
IOT GM

## Slide 20: Correlate GNSS KPIs
Chart: Clock adjustment - locked to GNSS
Expected
adjustment
window
KPI Monitoring (Location A) | Possible Events
Local clock | Rapid adjustment
Remote clock | MTIE outage
GNSS data | Suspected: Spoofing; Jamming; ...
KPI Monitoring (Location B) | Possible Events
Local clock | Rapid adjustment
Remote clock | MTIE outage
GNSS data | Suspected: Spoofing; Jamming; ...
KPI Monitoring (Location C) | Possible Events
GNSS V OCXO | Rapid adjustment
GNSS V Remote clock | MTIE outage
GNSS data | Suspected: Spoofing; Jamming; ...

## Slide 21: GNSS - threats are very real… (https://www.hs.fi/kaupunki/art-2000005863957.html)
Car trackers (victims)
Jamming - Detection avoidance
Spoofing - Alibi
Police ”Logfile on his Gps-watch stored the true time from the satellite”

## Slide 22: Conclusions GNSS is the best source of high accuracy time, but it takes addional effort to ensure robust service.
IOT-GM simplifies GNSS deployment
  Antenna with no RF
Backup over network is essential
  IOT-GMs on edge
  Distribute “Frequency” from core (ePRTC and Cs)
Monitor and correlate KPIs
  Use available information (“raw data”)

## Slide 23
Thank You

## Slide 25: Data available from GNSS receivers?
Google released GNSS raw data on Android. Also GNSS Analysis Tools to process and analyze raw data.
Raw measurement data shows the receiver clock to better than 1ppb precision.
Raw data allows insight into the signal environment and receiver behaviour
Chipset vendors provide API, but raw GNSS data ?
http://insidegnss.com/gnss-analysis-tools-from-google/

## Slide 26: Some of the Raw attributes available (Google GNSS)

## Slide 27: STRIKE3 – One effort to document and categorize GNSS threats.
Standardisation of GNSS Threat reporting and Receiver testing through International Knowledge Exchange, Experimentation and Exploitation
Funded by EU-H2020 programme (Galileo)
Fingerprinting jamming techniques focusing on the RF waveform
Field recording-> Lab analysis -> Test playback
D4.2 Draft standard for receiver testing against threats
  considers jamming interference only in GPS L1 / Galileo E1
http://www.gnss-strike3.eu/

## Slide 28: PRTC test from STRIKE3