## Slide 1: UTC as a time reference for industry Elizabeth Laier English Peter Whibberley Conway Langham David Hicks Simon Ashford Ali Ashkhasi Marivon Corbel

## Slide 2
A brief history of the national time scale
Atomic timekeeping and redefinition of the second
International Time today: UTC
The UK’s national time scale UTC(NPL)
Outline

## Slide 3
Railways drove the standardization of time across the UK in the 19th century
The electric telegraph provided the means to disseminate time from Greenwich from 1852
A brief history of the national time scale

## Slide 4
1884: International time
The International Meridian Conference in Washington DC:
Adopted Greenwich as the prime meridian
Recommended GMT as the reference time for the world
Proposed the time zones system
1 second = 1/86400 of the mean solar day
  -

## Slide 5
1950s: Variations seen in Earth’s rotation
Plot shows length of day in excess of 86400 SI seconds (LOD),
1962-2014 (Source: IERS)
3 ms
0 ms

## Slide 6
Start of atomic timekeeping
1955: Louis Essen and Jack Parry with the NPL Cs frequency standard, Accurate to 1 part in 1010 or 1s in 300 years
1958: International Atomic Time (TAI) Formed following the development of further caesium clocks in the USA and Switzerland
1960: Coordinated Universal Time (UTC) Introduced as the reference time scale for time broadcasts

## Slide 7
1960s: NPL caesium standards

## Slide 8
1967: Redefinition of the second
A new definition adopted for the second in the International System of units of measurement (SI):
The second is the duration of 9 192 631 770 periods of the radiation corresponding to the transition between the two hyperfine levels of the ground state of the caesium-133 atom.
Atomic time: Definition of the second is now based on an electron frequency transition of the caesium atom

## Slide 9
Leap second insertions
27 leap seconds since 1972,
all positive

## Slide 10
International Time Today - UTC
Computed by the International Bureau of Weights and Measures
  (BIPM – Bureau International des Poids et Mesures)
    Based at Sèvres, Paris

## Slide 11
Summary of how UTC is formed
Stability and resilience is achieved by averaging around 500 atomic clocks in around 70 institutes worldwide
The results are published monthly in BIPM Circular T and weekly ‘rapid’ results published in UTCr
The IERS decides on leap second insertions to keep UTC in step with the Earth’s rotation (UT1)
Accuracy is achieved using data from Cs fountain primary standards

## Slide 12
Local UTC(k)
time scales
~500 commercial
atomic clocks
Primary
Frequency
Standards
(PFS)
Free Atomic Time
(EAL)
International Atomic Time
(TAI)
Coordinated Universal Time
(UTC)
BIPM Circular T
Earth rotation
measurements
Universal Time
(UT1)
leap seconds
corrections to local
UTC time scales
BIPM
~70 National
Timing Institutes
IERS
Generation of UTC

## Slide 13
Institutes contributing to UTC
Source:
BIPM

## Slide 14
Properties of UTC
Not available in real time
Provides the reference for ALL civil and broadcast time scales, eg:
  GPS time (and other GNSS)
  Internet time (NTP)
  Radio time signals
Accessed via one of the approx. 70 UTC(k) institutes, eg. UTC(NPL)

## Slide 15
BIPM Circular T
Published monthly and gives UTC-UTC(k) results, for example:

## Slide 16
Circular T Results

## Slide 17
UTC(NPL) time scale
Based on a group of continuously-running commercial atomic clocks:
  5 active hydrogen masers and 4 caesium clocks

## Slide 18
NPL caesium fountains
Two operational fountains: NPL-CsF2
NPL-CsF3
Accuracy is 2.0 x 10-16
  20 ps/day
  Commercially available from NPL

## Slide 19
Comparing time scales (1): Two-way satellite time transfer
Geostationary Satellite
UTC(k1)
Satellite time transfer modems
Institute 1
Institute 2
UTC(k2)
Modem

## Slide 20
Satellite time transfer earth station
Signals are modulated with a pseudo-random noise (PRN) sequence containing a time marker
Operation is automated, with sessions every 2 hours
When calibrated, the method is accurate to 1 ns
Typical TWSTFT earth station is a Ku-band ‘VSAT’ (Very Small Aperture Terminal)
  NPL: Offset parabolic antenna 1.8 m diameter

## Slide 21
Comparing time scales (2): GPS common-view time transfer
GNSS time transfer receivers
Institute 1
UTC(k1)
Institute 2
UTC(k2)

## Slide 22
UTC Time dissemination from NPL
NPLTime service for UK financial sector using PTP over optical fibre links
MSF 60 kHz radio time signal, broadcast from Anthorn, Cumbria
NTP internet time service for synchronising computers

## Slide 23
NPLTime
NPLTime

## Slide 24
CLONETS
Clonets

## Slide 25
The future of UTC (1)
More and better primary standards
  - Optical clocks contributing in the next few years
Improved methods of time & frequency transfer
  Regional optical fibre networks
  Links using Atomic Clock Ensemble in Space (ACES) from Summer 2020

## Slide 26
The future of UTC (2)
Ending leap seconds?
  Debate over their future since 2000
  Will continue until at least 2023
  Still no agreement
Clocks on Earth limited by gravity changes
  Interest in more and better (optical) clocks in space
  Master clocks onboard geostationary satellites?

## Slide 30
Summary
UTC is the precise time scale in use world-wide
UTC combines the stability of atomic clocks (SI second) with a close link to mean solar time (UT1)
UTC is accessed through the time scales operated by contributing timing centres, eg. UTC(NPL)