## Slide 1: A Deep Dive Investigation into The Challenges of Sync Over DWDM Networks
Jon Baldry
ITSF – Düsseldorf – 8th November 2022

## Slide 2: Sychronization Distribution Strategies for 5G
In-band Delivery
Optical Timing Channel
In-band delivery of synchronization
Transponder synchronization performance
Coherent synchronization performance
High-performance PTP 1588 and SyncE delivery
Out-of-band delivery of synchronization
Very high-performance PTP 1588 and SyncE
Single-fiber CWDM and O/E/L-band overlay
OTC network elements:
  T-BC Class D boundary clocks
  Optical 3R regeneration
Hybrid Sync Distribution
Hybrid use of in-band and OTC mechanisms
Interoperable and interchangeable
All high-performance 1588 PTP, not proprietary
Use the appropriate solution for the best fit
  In-band delivery perfect for metro-access
  OTC widely used as core distribution
T-GM
T-GM
T-GM
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC/3R
T-BC/3R
T-BC/3R

## Slide 3: Creating an OTC2.0-enabled vPRTC/Timing Cloud
OTC2.0-ENABLED vPRTC:
Provides GNSS-like omnipresent timing, overcoming GNSS security/reliability/accessibility issues
Uses secure and reliable optical network to deliver highly-accurate timing/synchronization:
  Predictable, traceability to UTC and PRC
  Reliable, resilient and secure
  Highly-accurate, Class D in Timing Cloud
Flexible and independent
Every DWDM node capable of delivering timing/synchronization
Preserves timing budget for access/aggregation networks
Simplifies timing/synchronization planning and ongoing operations
Range of 100 ns vPRTC (Timing Cloud) resilient timing service
Redundant GNSS spoofing hardened GM/ Cesium source
5G Fronthaul /Midhaul
Other timing critical applications (power distribution, scientific)
vPRTC (Timing Cloud) with every DWDM node capable of delivering timing/synchronization
100 ns
5G Fronthaul /Midhaul

## Slide 4: Let’s Dive into The Challenges of Sync Over DWDM Networks

## Slide 5: 5G Drives High-accuracy Synchronization Requirements
ePRT/PRTC
15 ns - 100 ns
Transport Network 1000 ns
eCPRI Transport
60 ns - 190 ns
eREC
eRE
TDD/LTE-A and 5G macro phase services traceable to UTC
Inter antenna relative phase alignment
Network Budget
Max|TE|
4G
5G
4G
5G
CPRI
eCPRI
eCPRI
CPRI
CU
CU
MEC
MEC
MEC
PRTC/T-GM
ITU-T G.8273.2 PTP T-BC Class C
Fronthaul
Network
Midhaul
Network
ITU-T G.8275.1 Full Onpath Support
ITU-T G.8262.1 eEEC Synchronous Ethernet
3GPP TS 38.104 Time Alignment Error
ITU-T G.8271.1 Network Limits
DU
BBU
IP/MPLS Access DWDM
Fronthaul
Midhaul and Backhaul
5G
Ethernet
ITU-T G.8273.2 PTP T-BC Class B/C
ITU-T G.8275.1 Full Onpath Support
ITU-T G.8262.1 eEEC Synchronous Ethernet
Backhaul
Network
IP/MPLS Metro DWDM
IP/MPLS Core DWDM
T-TSC
T-TSC
IP Router or Ethernet Switch with inbuilt T-BC

## Slide 6: G.8271.1 Time Error Budget
A, B
C
D
G.8271.1 Network Reference Points
±100 ns
(PRTC/T-GM)
±200 ns dTE
(random network
variation)
node asymmetry
link asymmetry
compensation
Class A T-BCs:
Class B T-BCs:
Class C T-BCs:
±210 ns cTE (21 nodes @ ±10 ns per node)
±590 ns cTE (link asymmetry compensation)
±420 ns cTE (21 nodes @ ±20 ns per node)
±380 ns cTE
±250 ns cTE
±550 ns cTE (11 nodes @ ±50 ns per node)
±250 ns
(short term holdover)
±150 ns
(end application)
±1.5 µs end-to-end budget
±1.1 µs network equipment budget
ONLY 250-590 ns cTE AVAILABLE FOR THE DWDM TRANSPORT NETWORK

## Slide 7: Example Causes of Asymmetry in Optical Transport
Class C T-BC
Ethernet Switch
Fiber
Coherent Optics
OTN Mapping
Optical Devices
Coherent Optics
Optical Devices
OTN Mapping
Class C T-BC
Ethernet Switch
Fixed cTE components
Random cTE components
Random cTE components
Contributor | Fiber | Optical Devices (Dispersion Comp, OA/ILA, ROADM) | Coherent Optics | OTN Mapping | IP Routing and Ethernet Switching
Source | Asymmetry in fiber lengths, jumper cables, etc. 2.5 ns/m (vs 5 ns/m latency) | Random asymmetry in fiber lengths used in each direction | FIFO buffers in DSP Varies on restarts | Deep FIFO buffers in OTN mapping Varies on restarts | Traffic/buffering asymmetry and timestamping inaccuracy
Impact | Large but static | Very large but static | Varying and random | Large and random | Tight requirements to control impact
Range | Fixed cTE of ±5 to 1000+ ns | Fixed cTE of ±5 to 20,000 ns | Random cTE of ±20 to 130 ns on restart | Random cTE of ±20 to 1000 ns on restart | Class A/B/C specifications Max(TE) of 30 to 100 ns cTE of 10 to 50 ns dTE (low-pass filtered) of 10 to 40 ns

## Slide 8: FIFO Buffers and Their Impact on Sync Distribution
Electrical Domain
Optical Domain
Client Optics
Client Optics
Client Optics
Client traffic aggregation
OTN Mapper/ Framer
Coherent Optics (DSP)
WSS
OMD
λ1
λn
EDFA
EDFA
WSS
OSC
DCM
Deep buffers required for broad range of OTN client services
DCM
Source: Microchip
FIFO buffer cTE varies on restart/power cycles

## Slide 9: Real World DWDM Max Random cTE Measurements
OTN Mapping destroys cTE margin
OTN Mapping destroys cTE margin

## Slide 10: OSC vs OTC
Optical Supervisory Channel (OSC)
  Integrated and locked to OLS
  Pre-existing channel for management comms
    OSC not exclusive to timing, TE is heavily dependent on load due to scheduling
  Lower cost
  Lower performance
    Typically dual fiber (more cTE) with no asymmetry control
    Locked to existing wavelength
    Lower bandwidth (FastE) and shared
    No/limited interworking between platforms/vendors
Optical Timing Channel (OTC)
  Independent of OLS
  Dedicated and optically optimised sync/timing channel
  Higher cost
  Higher performance
    Single fiber (no additional cTE) with asymmetry and TE control
    Wavelength optimized for sync on span-by-span basis
    Higher bandwidth (GbE) and dedicated
    Platform/vendor agnostic
Electrical Domain
Client Optics
Client Optics
Client Optics
Client traffic aggregation
OTN Mapper/ Framer
Optical Domain
Coherent Optics (DSP)
WSS
OMD
λ1
λn
EDFA
EDFA
WSS
OSC
DCM
OTC
DCM
1 – In-band
2 – Wavelength
3 – OSC
4 – OTC

## Slide 11: Summary
Timing/Sync distribution over DWDM requires:
Multiple sync strategies
Timing channels optimized for sync distribution
Careful system level and network level design
High-performance timing/sync distribution over DWDM enables:
Highly reliable and resilient network timing/sync
vPRTC/Timing cloud architectures
Support for multiple applications – not just 5G

## Slide 12: Thank You