## Slide 1: Are you on time?
Verify PTP accuracy on pre-silicon ASICs
Nitzan Dror
Switch ASIC Architect
20/6/22

## Slide 2: Motivation
Time sync
  Mobile/5G networks
  Industrial networks (gPTP)
  Autonomous cars
Silicon inside
  Processor SOC
  NICs
  Switches

## Slide 3: Embedded PTP HW engines
Maintain the local time (TAI/TOD)
  Phase Update
  Frequency update
  Sync to a peer device (e.g. PPS)
Ingress / Egress timestamp

## Slide 4: Chips PTP HW Requirements
Accurate
  Symmetric
  Minimal PDV
A system is only as accurate as its underlying chip!

## Slide 5: Accuracy Requirements
Parameter | Measurement | Class C | Class D
Max ¦TE¦ | Unfiltered | 30 ns | -
Max ¦TEL¦ | Low pass | - | 5 ns

## Slide 6: What Can Go Wrong?
Timestamp with min PDV
(AM, multi-lane, IDLE, clk phases)
High frequency clk
Balanced time distribution (Symmetric)
HW clock frequency
cross
(min PDV)
Sample/Sync IO as close to pin

## Slide 7: Why Verify Before Manufacturing?
Metal fix at 5nm is ~M$
Tapeout at 5nm is ~10x M$
Complex bugs – re-development
*From quora
Notes: From Quora

## Slide 8: Motivation - Summary
Strict PTP accuracy requirements (small margin)
+
Complex design (high risk)
+
High penalty ($)
=
Verify PTP accuracy in pre-silicon

## Slide 9: How Should We Do It?
HW Simulation
Use a 3rd party (sim) traffic generator
  No PTP dedicated one
  Poor timestamp accuracy

## Slide 10: Test Topology #1 - OC
Target (DUT) clk == Source clk
Not good for pre si
  Slow convergence
  PTP Software application
    Heavy to simulate
    Not a part of the DUT
(DUT)
?
==
Target Clock
Source Clock

## Slide 11: Test Topology #2 – E2E TC
Timestamp latency PTP header (CF)
Real latency (sim time) = timestamped latency (CF)
How to measure real latency (on pins boundaries)?
  Traffic Gen – inaccurate
  Identify the start of packet on the SERDES
    Hard, especially with multiple encoding, lanes, FEC

## Slide 12: Where Does My Inaccuracy Come From?
Where the PDV is unaccounted for!
PDV beyond the timestamping points

## Slide 13: Our Solution
Measure PDV beyond the timestamping points
Use port loopback
Timestamp the packet on ingress & egress
  Time delta = latency = ingress timestamp – egress timestamp
  This latency variation is the inaccuracy
    Packet to packet
    Power up to power up (simulations)
X
OK
OK
DUT

## Slide 14: PROs
Covers PTP HW accuracy
Applicable for pre-silicon verification
  Quick convergence
  No SW needed
Applies the same to post-silicon
Allows for mix of PTP and background traffic
Same concept for all port modes/speeds
  Even encrypted PTP

## Slide 15: The Gory Details
Timestamp the packet on ingress & egress
  Time delta = latency = ingress timestamp – egress timestamp
Avg = average(latency)
  Over multiple PTP frames in a test
dTE = Max(|latency[i] - avg|, )
  Latency variation – between PTP frames (i=0,1,…) in a test
cTE = ( Max(avg[j]) – Min(avg[j]) ) / 2
  Average (latency) variation – between tests (j=0,1,…)
--------
Latency
*From Calnex

## Slide 16: Really, Does It Actually Work?
Marvell Switches are PTP Class D Accurate

## Slide 20: CONs
Rx & Tx inaccuracy is combined
Rare events require artificial speedup (e.g. AM)
  Make them more frequent
Doesn’t cover TAI/TOD updates
  Interfaces (PPS)
  Phase drift
  Freq/phase update
    Should be covered in TAI stand alone