## Slide 1
Optical Atomic Clocks for Stable UTC
Ekkehard Peik
Time and Frequency Department
PTB, Braunschweig, Germany
ITSF 2022, Düsseldorf, 10.11.2022

## Slide 2
The SI unit of time – the second – is defined as:
 until 1956 : the fraction 1/86 400 of the mean solar day
 1956 to 1967 : the fraction 1/31,556,925.9747 of the tropical year 1900
1 tropical year = 365,2422 solar days = 366,2422 sideral days
1967 : the duration of 9 192 631 770 periods of the radiation corresponding to the transition between the two hyperfine levels of the ground state of the cesium 133 atom Added in 1999: This definition refers to a cesium atom at rest at a temperature of 0 K
(Rewording in 2018)
Definitions of the SI unit of time and the scale unit of UTC
Astronomy
(angle/phase of a linear process)
Quantum physics
(frequency of a periodic process)

## Slide 3
Realization of the SI second with primary Cs frequency standards
Cs fountain accuracy  10-16
PTB fountain clocks
CSF1 and CSF2

## Slide 4
The era of Optical Frequency metrology
 Time to change the definition?
Optical Frequency Standards (Sr, Yb, Yb+, Al+, Ca+, …) at 10-18 level

## Slide 5
Secondary representations of the second
List of recommended standard frequencies (published on the BIPM website):
1 microwave (Rb) and 8 optical standards are recommended for applications as secondary representations of the second, with an uncertainty similar to primary Cs clocks.

## Slide 6
Monthly updated plot https://webtai.bipm.org/database/show_psfs.html
Contribution from Primary and Secondary Frequency Standards to TAI

## Slide 7: Optical Clocks: Improved Stability and Accuracy
Instability:
(Allan deviation)
At Dn=1 Hz, an optical single-ion clock (N=1) provides an instability sy≈10-15 (t/s)-1/2,
lower than a caesium fountain clock with Dn=1 Hz and 106 atoms.
Accuracy: Some systematic shifts that are determined by external fields and atomic properties and are relatively much smaller in the optical range:
relative shift for:
Cs 9.19 GHz Yb+ E3, 642 THz
quadrat. Zeeman shift at 1 mT 4.7 × 10-12 3.3 × 10-18
AC Stark of thermal radiation at 300 K -1.7 × 10-14 -7.1 × 10-17

## Slide 8: Clock ensemble in PTB‘s clock hall
Yb2
Yb1
CSF1
CSF2
Yb3
frequency comb
Yb/Sr

## Slide 9
Optical clock with a single laser-cooled ion in a Paul trap
Combined with laser cooling:
Lamb-Dicke confinement of a single ion
The ion trap provides long interaction and coherence times
quantum noise limited stability
high spectral resolution,
excellent control of systematic shifts
Hans Dehmelt

## Slide 10: Yb+ E3 clock comparison
six-month-long comparison
two clocks on the E3 transition 642 THz
different experimental setups
Yb1
Yb2
C. Sanner, N. Huntemann, R. Lange, Chr. Tamm, E. Peik, M. S. Safronova, S. G. Porsev, Nature 567, 204 (2019)
statistical uncertainty of 2.1 × 10-18

## Slide 11: Yb+(E3) vs Cs clock comparison
repeated measurements since 2017
Yb1(E3) and two caesium fountains
most accurate determination of an optical transition frequency
Yb1
CSF
R. Lange, N. Huntemann, J. M. Rahm, C. Sanner, H. Shao, B. Lipphardt, Chr. Tamm, S. Weyers, E. Peik, Phys. Rev. Lett. 126, 011102 (2021)

## Slide 12: Robust optical clock for users:
BMBF sponsored quantum-technology pilot project 2017-2020
Demonstrator of a turn-key optical clock for autonomous operation using 171Yb+ (E2)
Target market: superior H-Maser alternative (for NMIs, radio astronomy, ground station of GNSS, …)
physics package
6 companies, 4 institutes

## Slide 13: Evaluation of the clock
Comparison of opticlock with the lab clock Yb1 (E3)
Interrogation time: opticlock (E2): 40 ms,
Yb1(E3): 300 ms
Test run for 2 weeks with 99.8 % uptime
Systematic uncertainty 2  10-17
J. Stuhler et al., Measurement: Sensors 18, 100264 (2021)

## Slide 14
PTB Working Groups: Unit of Time / Optical Clocks with Trapped Ions
Yb+ clocks
N. Huntemann
R. Lange now: auto. Ind.
B. Lipphardt
Chr. Tamm
M. Steinel
M. Filzinger
C. Sanner now: JILA
M. Abdel Hafiz now: U. Franche Comté
Hu Shao now: CAS
Funding:
DFG, EURAMET, EU H2020
Thanks:
N. Dimarcq (CCTF)
P. Tavella (BIPM)
J. Stuhler (Toptica)
P. Schmidt (QUEST, PTB)
Cs clocks
S. Weyers
J. Rahm
M. Kazda
V. Gerginov now: NIST

## Slide 15
Physikalisch-Technische Bundesanstalt
Braunschweig and Berlin
Bundesallee 100
38116 Braunschweig, Germany
Dr. Ekkehard Peik
Head of Department Time and Frequency
E-Mail: ekkehard.peik@ptb.de
http://www.ptb.de/zeit/ http://www.ptb.de/time/