## Slide 1: Adding Resilience and Accuracy to GNSS
ITSF 2022 Düsseldorf, Germany

## Slide 2: Heiko Gerstung Managing Director, Meinberg heiko.gerstung@meinberg.de Tor Melgård Principal Innovation Engineer, Fugro t.melgard@fugro.com Ole Petter Rønningen Senior Innovation Engineer, Fugro o.ronningen@fugro.com Frank Boon Principal Innovation Engineer, Septentrio frank.boon@septentrio.com Jean-Marie Sleewaegen Systems Architect & Pricipal Signal Processing Expert, Septentrio jean-marie.sleewaegen@septentrio.com

## Slide 3: Agenda
GNSS Today
Weaknesses
Jamming and Spoofing
New Approach to Secure and Enhance GNSS
Continous monitoring of all SVs of all four major constellations
Computed orbital/timing corrections to improve performance
Integrity checks and detection of failing/misbehaving SV clocks in real time
State of Test Campaigns
UTC Traceability
First Commercial Implementation

## Slide 4: GNSS Today
Weaknesses and Vulnerabilities

## Slide 5: GNSS Weaknesses
Civil GNSS signals available for the general public are unencrypted and vulnerable to spoofing and jamming attacks.
Widely used to synchronize critical infrastructure (power grids, telecom networks, financial markets, media broadcasts).

## Slide 6: Jamming and Spoofing
Jamming relatively easy to detect (you will notice it) and mitigate (holdover is your friend)
Spoofing much more problematic unless detected (detected spoofing = jamming)

## Slide 7: New Approach
Adding Resilience and Accuracy to GNSS

## Slide 8: New Approach to Secure and Enhance GNSS
Enhance GNSS resilience and performance using data aquired by a large number of reference stations which is securely transmitted via geostationary satellites to end-user-devices.
Global coverage and very robust and reliable infrastructure both in space and on the ground.
Commercial implementation currently undergoing extensive tests and performance measurements.

## Slide 9: Reference Stations
Continuous reception of GNSS satellite signals at ~100 locations all around the world
Own independent timescale used to verify/measure timing parameters of satellites
All Reference stations together allow to collect data from every single GNSS satellite of the four constellations in real time
Anomalies and failures (e.g. SV clock misbehaving) can be detected immediately

## Slide 10: Control Centers
Each Control Center runs two independent software/firmware versions and operates 24/7 in a highly redundant configuration
Real time data of reference stations is collected, stored and analyzed in real-time
Precise orbit and clock corrections as well as timescale computed based on the received data
Correction values and state information for each SV of all four constellations are sent via Inmarsat to all end user devices

## Slide 11: End User Devices
Receiving GNSS signals for all four constellations
In addition, L-Band transmissions from geostationary satellites received
Verification of integrity of received GNSS SV data to detect spoofing attacks
Applies correction values for positioning and timing

## Slide 12: L-Band Satellite Transmission
Inmarsat satellite constellation consists of a number of geostationary satellites
Covers almost the whole planet, only exception is the pole regions
“Out of band” data transmission (independent of the GNSS signals)
Proven technology used widely for global satcom applications since 1979 (last launch of a new satellite in Dec 2021)
Data transmission protected by asymmetric cryptography (private/public keys)

## Slide 13: State of the Tests
Spoofing Protection and High-accuracy Measurements

## Slide 14: Spoofing Protection
Tests planned for Q4/2022 with independent lab
Not easy to test
  Most spoofing tests use GNSS simulator directly connected to antenna path
  L-Band signal needs to be added
  Looking for spoofing tests in protected areas
Results will be published in Q1/2023

## Slide 15: High-Accuracy Measurements (1)
Impressive timing improvements over standard GNSS: < 1ns over several weeks
Test campaign in cooperation with Norwegian NMI
Chart: Real-time clock comparison to AtomiChron and GPS timescale

## Slide 16: High-Accuracy Measurements (2)
Chart: Real-time clock comparison to timescale

## Slide 17: High-Accuracy Measurements (3)
Chart: Real-Time time transfer Darmstadt - Brussels

## Slide 18: Traceability to UTC
Comparing Time with UTC Clocks and Publishing Results

## Slide 19: Monitoring System Offset to UTC
System time is based on GNSS timescales (GPS, Galileo)
UTC reference stations
  Measure performance of service against local UTC reference clocks
  Logging offsets 24/7
  Publishing logs every day for the last 24 hours
Looking for interested NMIs

## Slide 20: Comparison UTC(ORB) - UTC(JV) using products from BIPM and AtomiChron

## Slide 21: First Commercial Implementation
Securing and Hardening GNSS for Timing

## Slide 22: First Implementation in 2023
Commercial Service with SLAs and Customer Support
Multiconstellation + Multiband GNSS receiver module based on Septentrio mosaic-T GNSS module
  Already included protection against spoofing and jamming in its base version
  Special Firmware developed by Septentrio to receive and decode Inmarsat L-Band Transmissions
  Clock Module for Meinberg Timing System verifies status of NMA and takes correction data into account to improve timing

## Slide 23
Thank You!