## Slide 2: Impressum
Title: COMPASSO
an in-orbit verification mission testing optical key technologies for future GNSS
Date: 10.11.2022
Autor: Dr. Johann Furthner
Institute: Galileo Competence Center
Figure credits: All Figures „DLR (CC BY-NC-ND 3.0)“

## Slide 3: Compasso an in-orbit verification mission testing optical key technologies for future GNSS

## Slide 4: COMPASSO
What does COMPASSO stand for?
  Development and validation of a new generation of high-precision optical clocks and laser terminals
What does COMPASSO make possible?
  Improvement of the Galileo overall system and the services it provides

## Slide 5: COMPASSO
Benefits of Optical Clocks for GNSS
  High short time (1-10 sec) stability comparing to RF clocks (DLR Iodine Clock: Allan Deviation 10-14 and better)
  EU sovereign technology IPR and production
  Robust in Space Environment
  Easy to maintain

## Slide 6: COMPASSO
Benefits of Optical Laser Terminals for GNSS
  Greater signal power with lighter and smaller components
  Significant higher data rate
  Bidirectional communication and ranging
  No ITU regulations required
  No interference / no jamming
  Lower bias error due to in-orbit calibration possibility
  Higher chip rate for faster and more precise ranging
  Robust against eavesdropping
  Optical technology can enable quantum key distribution for improved security

## Slide 7: COMPASSO Experiment: Optical Payload
Validation of Optical Technologies
  Laser terminals for communications and ranging
  High-precision optical clocks (iodine clock)
  Frequency comb for the optical range
OBJECTIVE:
Deployment on the Bartolomeo platform
on the International Space Station (ISS)
Partners
Institute of Communications
and Navigation
Institute for Software Technology
Space Operations
and Astronaut Training
Institute of Quantum Technologies
Institute of Space Systems
---------------------------------------------
Airbus
Tesat
Menlo
SpaceTech Immenstaad

## Slide 8: COMPASSO Core Elements
 | Frequency Comb (TRL 4)
mass | ~6.8 kg
power | ~35 W
Volume | ~7 l
 | LCRT (SmartLCT TRL 9, OSCAR TRL 4)
mass | ~ 47 kg
power | ~ 131 W
volume | ~80 l on platform, ~15 l outside
 | COMPASSO Iodine Reference (TRL 4)
mass | ~23 kg (incl. 20% margin)
power | ~57 W (incl. 20% margin)
volume | ~34 l (450 mm x 300 mm x 250 mm)

## Slide 9: COMPASSO Accomodation

## Slide 10: COMPASSO Input TRL
Iodine Frequency Reference
Frequency Comb
Optical System for Communication and Ranging
Laser Communication Terminal
OCXO
GNSS
Star Sensor
LCRT
Clock
PVAT
GNSS disciplined OCXO
COMPASSO

## Slide 11: COMPASSO Mission Timeline
~ 400 km
Bidirektional
Optical
Link
BBM
(DLR)
Development Models
Mission 2025/26
Return of Payload (2026)
Launch
End.2024
DM
(DLR)
FM
(Airbus)
Operation
Optical Ground
Station
4 Years
1,5 Years
2 Years
Test & Analysis
ISS
BBM: Breadboard Model; DM: Development Model; FM: Flight Model

## Slide 12: COMPASSO Impressions
Courtesy: NASA

## Slide 13: COMPASSO Impressions
Courtesy: NASA

## Slide 14: COMPASSO Impressions

## Slide 15: Thank you for your attention